## Slide 1: Introduction to Verilog
Programming Warm-up
Prepared by
Beig Rajibul Hasan
Lecturer, CSE, BRAC University
Contact: rajib.hasan@bracu.ac.bd

## Slide 2: Verilog HDL
Verilog HDL is a general-purpose hardware description language which can describe the digital circuits with C-like syntax.
Most popular logic synthesis tools support Verilog HDL.
Digital circuits can be described at the RTL of abstraction which ensures design portability.

## Slide 3
#include <stdio.h>
int main() {
  int num1, num2, sum;
  printf("Enter two integers: ");
  scanf("%d %d", &num1, &num2);
  // calculating sum
  sum = num1 + num2;
  printf("%d + %d = %d", num1, num2, sum);
  return 0;
}
Execution details of a simple C code
31 | 30 | …… | 1 | 0
31 | 30 | …… | 1 | 0
31 | 30 | …… | 1 | 0
$add num1, num2
……
……
PC
Instruction
register
Control
unit
……
num1
num2
sum
……
ALU
Instruction memory
Register file

## Slide 4: Basic building block of Verilog
A module is the basic building block of Verilog. A module consists of port declaration and Verilog codes to perform the desired functionality.
Ports are means for the Verilog module to communicate with other modules or interfaces. Ports can be of 3 types, such as: input, output, inout.
A typical Verilog module declaration:
module <name> (<ports_list>);
…
// Verilog Codes //
…
endmodule

## Slide 5
Verilog module and ports
Verilog module declaration
module and_or (x, y, a, b, c, d);
  input a, b, c, d;
  output x, y;
  …
  // Verilog Code //
  …
endmodule
Logic Synthesis
and_or
a
b
c
d
x
y

## Slide 6: Basic Syntax and Lexical Conventions
Documentation in Verilog code
- Documentation can be included in Verilog code by writing comments. A short comment begins with a double slash ( // ). A long comment spans multiple lines and is contained inside /* and */.
module and_or(x, y, a, b, c, d);
// A Verilog module
/*
This module takes four inputs a, b, c, d and produces two outputs x, y.
The outputs are defined as: x = (a & b) and y = (c | d).
*/
input a, b, c, d;
output x, y;
// Verilog Code for the desired functionality//
endmodule

## Slide 7: Basic Syntax and Lexical Conventions
White space
- White space characters such as SPACE and TAB are ignored by the Verilog compiler. Although multiple statements can be written in a single line, placing each statement in a single line and using indentation within blocks of code are good ways to increase readability of the code.
Number specification
- There are two types of number specifications found in verilog, sized and unsized.
- sized numbers are represented as: <size> ‘<base format> <number>. Supported formats are:
Base format | Illustration
d | decimal
b | binary
h | hexadecimal
o | octal

## Slide 8: Basic Syntax and Lexical Conventions
- If a number is specified without a base format, it is treated as a decimal number by the Verilog compiler.
- unsized numbers are specified without a size specification. unsized numbers are assigned a specific number of bits which is simulator and machine-specific (at least 32 bits).
Value Set
- Each individual signal/variable in Verilog can be assigned one
of 4 values:
sized number representation | unsized number representation
5’b10001 // This is a 5-bit binary number 4’hff01 // This is a 4-bit hexadecimal number 3’o123 // This is a 3-bit octal number 2’d10 // This is a 2-bit decimal number | 1254 // This is a 32-bit decimal number by default ‘h21ff // This is a 32-bit hexadecimal number ‘o345 // This is a 32-bit octal number ‘b1100 // This is a 32-bit binary number
Value level | Condition in Hardware
0 | logic 0 / False
1 | logic 1 / True
x | undefined
z | high impedance

## Slide 9: How to assign numerical values to the circuit nodes?
Verilog makes use of the reserved keyword assign to easily store numerical values in a variable.
The assign statements are concurrent, meaning that they are executed in parallel.
module in_disp(out, in); // This module implements a 1-bit buffer input in; output out; assign out = in; endmodule
in_disp

## Slide 10: Basic Syntax and Lexical Conventions
Identifier Names
Identifiers are the names of variables and other elements in Verilog code.
Valid identifier can include any letter and digit as well as “_” and “$” characters. There are two restrictions too , an identifier must not begin with a digit and it should not be a Verilog keyword. Furthermore, Verilog is case sensitive.
Identifier name | Validity
x1 | Valid
x_y | Valid
1x | Invalid
+y | Invalid
x*y | Invalid
258 | Invalid
ex_$1 | Valid

## Slide 11: Basic Syntax and Lexical Conventions
Vectors
- input or output variables can also be declared as vectors (multiple bit widths). If bit width is not specified, the default is scalar (1-bit).
- The multibit variables or vectors in general can be declared in Verilog using the syntax:
<data type> <MSB bit index : LSB bit index> <name>
module in_disp(out, in);
// This module implements a 3-bit buffer
input [2:0]in;
output [2:0]out;
assign out = in;
endmodule

## Slide 12: Verilog operators
Operator | Operation
~A | This will produce 1’s complement of A
A & B | Bitwise AND
A ¦ B | Bitwise OR
A^B | Bitwise XOR
A+B | Addition of two single or multibit numbers
A-B | Subtraction of two single or multibit numbers
A*B | Multiplication of two single or multibit numbers
A/B | Division of two single or multibit numbers
A%B | This returns the remainder of the integer division A/B
Below is a list of the most frequently used operators in Verilog:

## Slide 13
module and_or(x, y, a, b, c, d);
  input a, b, c, d;
  output x, y;
  assign x = a & b;
  assign out = c | d;
endmodule
CSE460 : VLSI Design
A simple circuit
and_or

## Slide 14: Another simple circuit
x1 | x2 | x3 | f
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
example_ckt
module example_ckt(f, x1, x2, x3);
  input x1, x2, x3;
  output f;
  assign g = x1 & x2;
  assign y = ~x2;
  assign h = y & x3;
  assign f = g | h;
endmodule

## Slide 15
Thank You
CSE460 : VLSI Design