## Slide 1: CSE 460: VLSI Design (Lab)
Experiment 3
Simulation of Mealy and Moore Type FSMs in Verilog

## Slide 2: Finite State Machine
In Combinational logic circuits, outputs are determined solely by the present values of the inputs.
In Sequential circuits, outputs depend both on the past behavior of the circuit and the present values of the inputs. The storage elements in terms of flip-flops can reserve the state information of the logic circuit at any given time.
The sequential circuits in which a clock signal is used to control the operation of the circuit, is called synchronous sequential circuits. These synchronous sequential circuits are known in general as Finite State Machines (FSMs).
The building blocks of a finite state machine are combinational circuits and one or more flip-flops. Under the control of the clock signal, the flip-flops change their state as determined by the combinational logic.
Combinational
circuit
Combinational
circuit
Flip-flops
W
Clock
Z
Q

## Slide 3
FSMs can be of two types:
Moore type FSM
  The sequential circuits whose outputs depend only on the states of the circuit are of Moore type.
Mealy type FSM
  The sequential circuits whose outputs depend on both the state and the present primary inputs are of Mealy type
Combinational
circuit
Combinational
circuit
Flip-flops
W
Clock
Z
Q
Finite State Machine

## Slide 4: FSM based motor speed controller
Comparator
Compares the accelerometer reading with the preset reference speed and outputs if the motor speed exceeds the reference value
Finite State Machine (FSM)
Based on the comparator output the FSM will enable the speed controller if for two consecutive clock cycles
Speed Controller
Reduces the motor speed if the output from the FSM is high i.e.
Accelerometer
Motor speed
(rpm)
w
z
DC motor

## Slide 5: Moore Type FSM
Problem:
Suppose that we wish to design a circuit that meets the following specification:
  The circuit has one input, w, and one output, z.
  All changes in the circuit occur on the positive edge of a clock signal.
  The output z is equal to 1 if during two immediately preceding clock cycles the input w was equal to 1. Otherwise, the value of z is equal to 0.
Input-output combination:

## Slide 6: Moore Type FSM
Figure : State Diagram
Present State | Next State |  | Output z
 | w=0 | w=1 | 
A | A | B | 0
B | A | C | 0
C | A | C | 1
Figure : State Table
Reset

## Slide 7: Moore Type FSM
Present State | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d
 | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d
Figure : State Diagram
Reset

## Slide 8: General Circuit Diagram of the FSM
Combinational
circuit
Combinational
circuit
FF-1
FF-2
Present State | Next State |  | Output z
 | w=0 | w=1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 00 | 10 | 1
11 | dd | dd | d
 | Next State |  | Output z
 | w=0 | w=1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 00 | 10 | 1
11 | dd | dd | d
Clock

## Slide 9: Designing the FSM in Verilog
In order to design the FSM using Verilog we will need to perform the following steps:
  Assigning binary variables to states
  A mechanism for figuring out the current state (Sequential circuit block)
  Defining the logic for state transition (Combinational circuit block)
  Defining the output for the current state (Continuous assignment statement)
always@(*)
begin
  C = A & B;
end
FF
always@(posedge clk) begin
  Q <= D;
end
Combinational circuit synthesis in Verilog
  always@(*)blocks are used to describe combinational logic in Verilog. Blocking assignment statements are to be used inside these blocks.
Sequential circuit synthesis in Verilog
  always@(posedge clk) or always@(negedge clk) blocks are used to describe combinational logic in Verilog. Non-blocking assignment statements are to be used inside these blocks.

## Slide 10: Moore Type FSM
Present State | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d
 | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d

## Slide 11: Moore Type FSM

## Slide 12: Mealy Type FSM
Problem:
We wish to design a circuit that meets the following specification:
  The circuit has one input, w, and one output, z.
  All changes in the circuit occur on the positive edge of a clock signal.
  The output z is equal to 1 if during two immediate clock cycles the input w was equal to 1. Otherwise, the value of z is equal to 0.
Input-output combination:

## Slide 13: Mealy Type FSM
Figure : State Diagram
/
/
/
/
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
A | A | B | 0 | 0
B | A | B | 0 | 1
Figure : State Table
Reset

## Slide 14: Mealy Type FSM
Figure : State Table
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
A | A | B | 0 | 0
B | A | B | 0 | 1
Figure : State-assigned Table
Present State | Next State |  | Output z | 
y |  |  |  | 
 | w=0 | w=1 | w=0 | w=1
 | Y | Y |  | 
0(A) | 0(A) | 1(B) | 0 | 0
1(B) | 0(A) | 1(B) | 0 | 1

## Slide 15: Mealy Type FSM
Present State | Next State |  | Output z | 
y |  |  |  | 
 | w=0 | w=1 | w=0 | w=1
 | Y | Y |  | 
0(A) | 0(A) | 1(B) | 0 | 0
1(B) | 0(A) | 1(B) | 0 | 1

## Slide 16: Mealy Type FSM

## Slide 17: An Example
Problem: Derive the state diagram for an FSM that has an input w and an output z. The machine has to generate z = 1 when the previous four values of w were 1001 or 1111; otherwise, z = 0.Overlapping input patterns are allowed. An example of the desired behavior is
Clock cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
w | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
z | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 18
State diagram(Moore type)
Reset

## Slide 19
Present State | Next State |  | Output z
 | w=0 | w=1 | 
S0 | S0 | S1 | 0
S1 | S5 | S2 | 0
S2 | S5 | S3 | 0
S3 | S5 | S4 | 0
S4 | S5 | S4 | 1
S5 | S6 | S1 | 0
S6 | S0 | S7 | 0
S7 | S5 | S2 | 1
Figure : State Table
Present State | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
 | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
Figure : State-assigned Table
State table (Moore type)

## Slide 20: State assigned table (Moore Type)
Present State | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
 | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1

## Slide 21: Timing diagrams (Moore Type)
Figure : Output waveform

## Slide 22: An Example
Problem: Derive the state diagram of the Mealy version for the example FSM that is, the FSM will generate at the instant the input values of have the pattern or . Overlapping of the input patterns are allowed.
Clock cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
w | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 23
/
/
/
/
/
/
/
/
/
/
/
/
State diagram(Mealy type)
Reset

## Slide 24
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
S0 | S0 | S1 | 0 | 0
S1 | S4 | S2 | 0 | 0
S2 | S4 | S3 | 0 | 0
S3 | S4 | S3 | 0 | 1
S4 | S5 | S1 | 0 | 0
S5 | S0 | S1 | 0 | 1
Figure : State Table
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
State table (Mealy type)

## Slide 25: State assigned table (Mealy type)
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
Figure : Verilog code (part 1)
Figure : State-assigned Table

## Slide 26: State assigned table (Mealy type)
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
Figure : Verilog code (part 2)

## Slide 27: Timing diagrams (Mealy Type)
Figure : Output waveform